## Slide 1: How to Prepare for Rental Inspections

## Slide 2: Goals
City of Duluth Rental License Requirements
Overview of the Codes
  History
  Regulations/Which Codes
Inspection Process
Common Code Corrections
Best Practices

## Slide 3: Duluth Fire Department Life Safety Division
Number of rental licenses
  Over 17,500 Units
  Over 15,000 Licenses
  40% of residences are rentals
Staff
  Lead Housing Inspector
  5-Housing Inspectors
  Solid Waste Compliance Officer
  Police Officer
  2-Office Staff
  Blight Mitigation Specialist

## Slide 4: License Fees-New Licenses
One Family Dwelling
Two Family Dwelling (Duplex)
  Rental License Base Fee: $320.
  $40 Fee Per Bedroom:
  Conversion Fee: $1500.
  Off-Street Parking Required
    Must install O.S.P.
    $100.00 fee per required space if not provided.
  No Conversion Fee
  Rental License Fee: $320.
  $40 Fee Per Bedroom
  Off-Street Parking Required
    Must install O.S.P.
    $100.00 fee per required space if not provided.

## Slide 5: 3+ units (multi dwellings)
$320 Base fee
$40 per unit
No parking requirements

## Slide 6: Rental License
Allows owner to rent to anyone for 30 days or more
3-Year License Cycle
  Inspection
License renewal sent out 3 months prior to expiration

## Slide 7: Bedrooms
Existing: Maximum 6 bedrooms per unit.
New: After August, 2017 bedrooms are capped at 4 per unit for new rental properties if adequate off-street parking is available. Up to 5 bedrooms are allowed if the property is recorded with the Assessor as having a minimum of 2500 sq.ft. of finished space as of August, 2017

## Slide 8: Parking Requirements
Off-Street Parking
(Single Family and Duplex)
Minimum of two off-street parking spaces required
After two spaces, one less than the bedroom count.
  3-bedrooms=2 O.S.P.
  4-bedrooms=3 O.S.P.

## Slide 9: Parking Spaces

## Slide 10: Code History and purpose
Purpose
  Codes were created based on property damage, injury or death
  Large devastating fire events
  Regulate and standardize construction/fire protection/maintenance
  Protect the health and safety of the public

## Slide 11: Rental Inspection codes
International Property Maintenance Code
  Model Code
  Minimum Maintenance and Safety Code for Existing Buildings
  Light, Ventilation, Plumbing, Heating, Interior/Exterior, Fire, Sanitation, Electrical
  3-Year Modification Cycle

## Slide 12: Other codes
Building Code/Existing Building Code
Minnesota State Fire Code
Other

## Slide 13: Duties
Inspect all rental housing
Investigate Unlicensed Rental Properties
Investigate Complaints
Repairs
Lack of Heat
Condemn Properties
Lack of Utilities
Unsafe/Unsanitary Conditions
Fire Damage
Structural Damage
Investigate and Enforce Solid Waste Violations

## Slide 14: Preparing for Inspections
Notify Tenants
Proactive Visit
Check all Smoke and Carbon Monoxide Alarms
  Battery
  Expiration Date
If maintenance is required, have a plan, and share with inspector

## Slide 15: Preparing for md inspections
Clear all hallways, corridors, stairways
Have Sprinkler System, Fire Extinguishers and Fire Alarm Inspected

## Slide 16: Common Code Requirements for Rental Licensing

## Slide 17: Interior
Peeling, chalking, flaking paint
Flooring-Free form tears, holes, etc.
Handrails and guards on stairs
  More than 4 risers
  Not less than 30” in height
  Guards required where walking surface is more than 30” to floor or grade below.

## Slide 18: Windows
Cracked Glass
(may not be replaced with plexiglass)
Windows
Every window, other than a fixed window, shall be easily openable and capable of being held open by window hardware (as designed).

## Slide 19: Doors
304.18.1 Doors – Deadbolt locks on rental, leased or sublet dwelling units.
  – Openable from side from which egress is to be made without the need for keys, special knowledge or effort.
    – Lock throw of not less than 1”.
    – Maintained in good working condition.
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 20: Extension cords
Cannot be used for permanent power
Cannot be daisy chained
May not be used for appliances, space heaters, etc
Power Strips with overload protection (20 AMP rated) allowed.

## Slide 21: Dryer Venting
No Plastic Vent lines
4” in diameter with two 90 degree elbows terminating outside
Back draft damper
No lint traps, heat diverters, or screens

## Slide 23: Water Heater
Connections maintained
Panels Intact
Overflow tube/pipe metal or copper and within 18” of the ground.
Smokepipe has positive slope to chimney or power vented

## Slide 24: smokepipe

## Slide 25: Outlets
All 3-Prong Outlets Must Be Grounded
Existing 2-Prong Outlets Permitted
Replacement of existing outlets requires ARC Fault and/or GFCI Protection based on outlet location

## Slide 26: Outlets/receptacles
Check available outlets for proper grounding and damage/failure

## Slide 27: Gfci: GROUND FAULT CIRCUIT INTERUPTER AFCI: ARC FAULT CIRCUIT INTERUPTER
GFCI
AFCI
AFCI/GFCI
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 28: Afci and GFCI Locations

## Slide 29: ELECTRICL SERVICE PANEL

## Slide 30: Water Supply System
505.3-The water supply system shall be installed and maintained to provide a supply of water to plumbing fixtures, devices and appurtenances in sufficient volume and at pressures adequate to enable to fixture to function properly, safely and free from defects and leaks.
Check for leaks, cracks, bad connections.
Low Water Pressure

## Slide 31: Premise Numbers
304.3 Premises identification. Buildings shall have approved address numbers placed in a position to be plainly legible and visible from the street or road fronting the property. These numbers shall contrast with their background. Address numbers shall be Arabic numerals or alphabet letters. Numbers shall be a minimum of 4 inches (102 mm) in height with a minimum stroke width of 0.5 inch (12.7 mm).

## Slide 32: Smoke Alarm Requirement (Single Family/Duplex)
Locations
  On Each Floor
  Outside Each Bedroom
  Inside Each Bedroom

## Slide 33: Smoke Alarm Requirement Mounting area
Mounting Area
  Wall-4” to 12” from the ceiling
  Ceiling-4” from the wall

## Slide 34: Alarm Types
Photoelectric
Detect visible fire particles (associated with slow smoldering fires) sooner than ionization alarms. These detectors are more sensitive to the large combustion particles that emanate during slow, smoldering fires, which usually occur at night when people are asleep before the source of the fire bursts into flames.
Ionization
  Detect invisible fire particles (associated with fast flaming fires) sooner than photoelectric alarms such as cooking fires or fires fueled by paper or flammable liquids.

## Slide 35: 10 year smoke alarms

## Slide 36: Smoke Alarm Statistics
When smoke alarms were present in fires considered large enough to activate them, they operated 87% of the time.
Three out of five home fire deaths resulted from fires in properties without alarms or non-working smoke alarms.
  Almost two out of five (38%) home fire deaths resulted from fires in which no smoke alarms were present at all.
  One of every five (21%) deaths was caused by fires in properties in which smoke alarms were present but failed to operate. (Battery Operated and Interconnected Alarms are Best)
  Smoke alarms operated in fires that caused two out of five (40%) home fire deaths.
  One percent of the deaths resulted from fires that were too small to activate the smoke alarm.

## Slide 37: !!!!!!!!!!!!!!!!!!!!!!!!!!!
The risk of dying in reported home structure fires is cut in half in homes with working smoke alarms

## Slide 38: Fire Causes-Cooking

## Slide 39: Fire Safety Requirements-Chapter 7
701.1 Scope. The provisions of this chapter shall govern he minimum conditions and standards for fire safety relating to structure and exterior premises including fire safety facilities and equipment to be provided.
Multi-Unit Buildings
  2A10BC Sized Extinguisher within 75’ of every apartment door
  OR inside each unit
Serviced/Inspected Annually
  Tagged
  Charged (Green)
  Mounted

## Slide 40: Fire Stop

## Slide 41: Fire Causes-Heating

## Slide 42: Fire Causes-Dryers

## Slide 43: CLOSING BEDROOM DOORS
When sleeping keep bedroom doors closed
  Slows entry of fire and smoke
  Allows extra time for escape

## Slide 44: Carbon Monoxide Alarms
Required within 10’ of every bedroom.
(no height requirements)

## Slide 45: Heat
Maintained and functioning properly
Maintain at least 68 degrees (October 15th thru May 15th)

## Slide 46: Fire Code Requirements
3’ Clearance around gas appliances
Self Closing doors between garages and habitable areas
All emergency escapes cannot be obstructed or locked.

## Slide 47: Fire Code Requirements
One-Hour Fire Resistive separation between floors and units
One-Hour Fire Resistive Corridors
5/8 Type “x” Gypsum Wallboard between habitable spaces
20 Minute Fire Door Assemblies for Corridors equipped with self-closing devices

## Slide 48: exterior
Rotting Shingle/Roof
Deteriorated Stairs
Missing/Deteriorated Flashing
Peeling paint

## Slide 49: Tenant Complaints
Tenant must submit complaint/request to owner/landlord in writing.
No action by landlord
  Life Safety Inspection
  Correction Order
Resources
  Tenant/Landlord Rights.
  One Roof Housing Mediation
  JUSTICE NORTH (formerly Legal Aid).

## Slide 50: Lack of compliance
Fees
Citations
  Criminal
      Civil/Monetary
Revocation
Condemnation
This Photo by Unknown Author is licensed under CC BY

## Slide 51: Questions